## Slide 1: Internet Security: How the Internet works and some basic vulnerabilities
Dan Boneh
CS 155

## Slide 2: Internet Infrastructure
Backbone
ISP
ISP
Local and interdomain routing
  TCP/IP for routing and messaging
  BGP for routing announcements
Domain Name System
  Find IP address from symbolic name (www.cs.stanford.edu)

## Slide 3: TCP Protocol Stack
Application
Transport
Network
Link
Application protocol
TCP protocol
IP protocol
Data Link
IP
Network Access
IP protocol
Data Link
Application
Transport
Network
Link

## Slide 4: Data Formats
Application
Transport (TCP, UDP)
Network (IP)
Link Layer
Application message - data
TCP
data
TCP
data
TCP
data
TCP Header
data
TCP
IP
IP Header
data
TCP
IP
ETH
ETF
Link (Ethernet)
Header
Link (Ethernet)
Trailer
segment
packet
frame
message

## Slide 5: Internet Protocol
Connectionless
  Unreliable
  Best effort
Notes:
  src and dest ports not parts of IP hdr
IP
Version
Header Length
Type of Service
Total Length
Identification
Flags
Time to Live
Protocol
Header Checksum
Source Address of Originating Host
Destination Address of Target Host
Options
Padding
IP Data
Fragment Offset

## Slide 6: IP Routing
Typical route uses several hops
IP: no ordering or delivery guarantees
Meg
Tom
ISP
Office gateway
121.42.33.12
132.14.11.51
Source
Destination
Packet
121.42.33.12
121.42.33.1
132.14.11.51
132.14.11.1

## Slide 7: IP Protocol Functions (Summary)
Routing
  IP host knows location of router (gateway)
  IP gateway must know route to other networks
Fragmentation and reassembly
  If max-packet-size less than the user-data-size
Error reporting
  ICMP packet to source if packet is dropped
TTL field: decremented after every hop
  Packet dropped if TTL=0.
  Prevents infinite loops.

## Slide 8: Problem: no src IP authentication
Client is trusted to embed correct source IP
  Easy to override using raw sockets
  Libnet: a library for formatting raw packets with arbitrary IP headers
Anyone who owns their machine can send packets with arbitrary source IP
  … response will be sent back to forged source IP
Implications: (solutions in DDoS lecture)
  Anonymous DoS attacks;
  Anonymous infection attacks (e.g. slammer worm)

## Slide 9: Transmission Control Protocol
Connection-oriented, preserves order
  Sender
    Break data into packets
    Attach packet numbers
  Receiver
    Acknowledge receipt; lost packets are resent
    Reassemble packets in correct order
TCP
Book
Mail each page
Reassemble book
19
5
1
1
1

## Slide 10: TCP Header (protocol=6)
Source Port
Dest port
SEQ Number
ACK Number
Other stuff
U
R
G
P
S
R
A
C
K
P
S
H
S
Y
N
F
I
N
TCP Header

## Slide 11: Review: TCP Handshake
C
S
SYN:
SYN/ACK:
ACK:
Listening
Store SNC , SNS
Wait
Established
SNC⟵randC
ANC⟵0
SNS⟵randS
ANS⟵SNC
SN⟵SNC+1
AN⟵SNS
Received packets with SN too far out of window are dropped

## Slide 12: Basic Security Problems
1. Network packets pass by untrusted hosts
  Eavesdropping, packet sniffing
  Especially easy when attacker controls a machine close to victim (e.g. WiFi routers)
2. TCP state easily obtained by eavesdropping
  Enables spoofing and session hijacking
3. Denial of Service (DoS) vulnerabilities
  DDoS lecture

## Slide 13: Why random initial sequence numbers?
Suppose initial seq. numbers (SNC , SNS ) are predictable:
  Attacker can create TCP session on behalf of forged source IP
  Breaks IP-based authentication (e.g. SPF, /etc/hosts )
    Random seq. num. do not prevent attack, but make it harder
Victim
Server
SYN/ACK dstIP=victim
SN=server SNS
ACK
srcIP=victim
AN=predicted SNS
command
server thinks command is from victim IP addr
attacker
TCP SYN
srcIP=victim
Notes: Example commands: send spam email on behalf of victim IP address
SPF: Sender Policy Framework

## Slide 14: Example DoS vulnerability: Reset
Attacker sends a Reset packet to an open socket
  If correct SNS then connection will close ⇒ DoS
  Naively, success prob. is 1/232 (32-bit seq. #’s).
    … but, many systems allow for a large window of acceptable seq. #‘s. Much higher success probability.
  Attacker can flood with RST packets until one works
Most effective against long lived connections, e.g. BGP

## Slide 15: Routing Security
ARP, OSPF, BGP

## Slide 16: Interdomain Routing
connected group of one or more Internet Protocol prefixes under a single routing policy (aka domain)
OSPF
BGP
Autonomous System
earthlink.net
Stanford.edu
(AS#4355)
(AS#32)
Notes: OSPF: open shortest path first

## Slide 17: Routing Protocols
ARP (addr resolution protocol): IP addr ⟶ eth addr Security issues: (local network attacks)
  Node A can confuse gateway into sending it traffic for Node B
  By proxying traffic, node A can read/inject packets into B’s session (e.g. WiFi networks)
OSPF: used for routing within an AS
BGP: routing between Autonomous Systems Security issues: unauthenticated route updates
  Anyone can cause entire Internet to send traffic for a victim IP to attacker’s address
    Example: Youtube-Pakistan mishap (see DDoS lecture)
  Anyone can hijack route to victim (next slides)
Notes: OSPF: open shortest path first

## Slide 18: BGP example [D. Wetherall]
3
4
6
5
7
1
8
2
7
7
2 7
2 7
2 7
3 2 7
6 2 7
2 6 5
2 6 5
2 6 5
3 2 6 5
7 2 6 5
6 5
5
5

## Slide 19: Security Issues
BGP path attestations are un-authenticated
  Anyone can inject advertisements for arbitrary routes
  Advertisement will propagate everywhere
  Used for DoS, spam, and eavesdropping (details in DDoS lecture)
  Often a result of human error
Solutions:
RPKI: AS obtains a certificate (ROA) from regional authority (RIR) and attaches ROA to path advertisement. Advertisements without a valid ROA are ignored. Defends against a malicious AS (but not a network attacker)
SBGP: sign every hop of a path advertisement
Notes: RIR: Regional Internet Registries (assign IP blocks to AS’s)
ROA: Route Origin Authorizations. Contains: AS number (ASN), validity date range, IP prefixes.
ROA says that an ASN is authorized to advertise for specific prefixes.

## Slide 20: Example path hijack (source: Renesys 2013)
Feb 2013: Guadalajara ⟶ Washington DC via Belarus
Normally: Alestra (Mexico) ⟶ PCCW (Texas) ⟶ Qwest (DC)
Reverse route (DC ⟶ Guadalajara) is unaffected:
Person browsing the Web in DC cannot tell by traceroute that HTTP responses are routed through Moscow
route in effect
for several hours
Notes: Path from DC to Guadalajara is unchanged. Only return path is changed.
More like this: Nov. 2014, March 2015.

## Slide 21: OSPF: routing inside an AS
Link State Advertisements (LSA):
Flooded throughout AS so that all routers in the AS have a complete view of the AS topology
Transmission: IP datagrams, protocol = 89
Neighbor discovery:
Routers dynamically discover direct neighbors on attached links --- sets up an “adjacenty”
Once setup, they exchange their LSA databases

## Slide 22: Example: LSA from Ra and Rb
Ra
LSA DB:
Rb
Rb LSA
R3
Ra
Rb
Net-1
Net-1
Ra LSA
Ra
Rb
Net-1
3
2
2
3
1
1
1
Notes: Ra and Rb send an LSA about the connection between them. That LSA is received by R3 and it updates its own LSA database.

## Slide 23: Security features
OSPF message integrity (unlike BGP)
  Every link can have its own shared secret
  Unfortunately, OSPF uses an insecure MAC:
    MAC(k,m) = MD5(data ll key ll pad ll len)
Every LSA is flooded throughout the AS
  If a single malicious router, valid LSAs may still reach dest.
The “fight back” mechanism
  If a router receives its own LSA with a newer timestamp than the latest it sent, it immediately floods a new LSA
Links must be advertised by both ends

## Slide 24: Still some attacks possible [NKGB’12]
Threat model:
single malicious router wants to disrupt all AS traffic
Example problem: adjacency setup need no peer feedback
LAN
Victim (DR)
a remote attacker
adjacency
adjacency
False Hello and DBD messages
net 1
phantom router
adjacency
Result: DoS on net 1
Notes: A router can setup an adjacency with a peer router without ever hearing back from the peer. Therefore, a remote attacker can cause a victim router to setup an adjacency with a phantom peer, resulting in DoS.

## Slide 25: Domain Name System

## Slide 26: Domain Name System
Hierarchical Name Space
root
edu
net
org
uk
com
ca
wisc
ucb
stanford
cmu
mit
cs
ee
www
DNS

## Slide 27: DNS Root Name Servers
Hierarchical service
  Root name servers for top-level domains
  Authoritative name servers for subdomains
  Local name resolvers contact authoritative servers when they do not know a name

## Slide 28: DNS Lookup Example
Client
Local DNS resolver
root & edu
DNS server
stanford.edu
DNS server
www.cs.stanford.edu
NS stanford.edu
www.cs.stanford.edu
NS cs.stanford.edu
A www=IPaddr
cs.stanford.edu
DNS server
DNS record types (partial list):
- NS: name server (points to other server)
- A: address record (contains IP address)
- MX: address in charge of handling email
- TXT: generic text (e.g. used to distribute site public keys (DKIM) )

## Slide 29: Caching
DNS responses are cached
  Quick response for repeated translations
  Note: NS records for domains also cached
DNS negative queries are cached
  Save time for nonexistent sites, e.g. misspelling
Cached data periodically times out
  Lifetime (TTL) of data controlled by owner of data
  TTL passed with every record

## Slide 30: DNS Packet
Query ID:
  16 bit random value
  Links response to query
(from Steve Friedl)

## Slide 31: Resolver to NS request
Notes: SBCglobal DNS resolver wants www.unixwiz.net. First queries C tld server.

## Slide 32: Response to resolver
Response contains IP addr of next NS server
(called “glue”)
Response ignored if unrecognized QueryID
Notes: Response points to two name servers.

## Slide 33: Authoritative response to resolver
final answer
bailiwick checking:
response is cached if it is within the same domain of query (i.e. a.com cannot set NS for b.com)
Notes: NS linux.unixwiz.net provides the final answer. Response passes bailiwick checking and will be cached.

## Slide 34: Basic DNS Vulnerabilities
Users/hosts trust the host-address mapping provided by DNS:
  Used as basis for many security policies:
  Browser same origin policy, URL address bar
Obvious problems
  Interception of requests or compromise of DNS servers can result in incorrect or malicious responses
    e.g.: malicious access point in a Cafe
  Solution – authenticated requests/responses
    Provided by DNSsec … but few use DNSsec

## Slide 35: DNS cache poisoning (a la Kaminsky’08)
Victim machine visits attacker’s web site, downloads Javascript
user
browser
local
DNS
resolver
Query:
a.bank.com
a.bank.com
QID=x1
attacker
attacker wins if ∃j: x1 = yj
response is cached and attacker owns bank.com
.com
response
256 responses:
Random QID y1, y2, …
NS bank.com=ns.bank.com
A ns.bank.com=attackerIP

## Slide 36: If at first you don’t succeed …
Victim machine visits attacker’s web site, downloads Javascript
user
browser
local
DNS
resolver
Query:
b.bank.com
b.bank.com
QID=x2
attacker
256 responses:
Random QID y1, y2, …
NS bank.com=ns.bank.com
A ns.bank.com=attackerIP
attacker wins if ∃j: x2 = yj
response is cached and attacker owns bank.com
.com
response
success after ≈ 256 tries (few minutes)
Notes: Birthday paradox: success once xi = yj for some i,j .
Success probability after each try is 1/256  needs 256 tries on average until success

## Slide 37: Defenses
Increase Query ID size. How?
Randomize src port, additional 11 bits
    Now attack takes several hours
Ask every DNS query twice:
  Attacker has to guess QueryID correctly twice (32 bits)
  … but Apparently DNS system cannot handle the load

## Slide 38: DNS poisoning attacks in the wild
January 2005, the domain name for a large New York ISP, Panix, was hijacked to a site in Australia.
In November 2004, Google and Amazon users were sent to Med Network Inc., an online pharmacy
In March 2003, a group dubbed the "Freedom Cyber Force Militia" hijacked visitors to the Al-Jazeera Web site and presented them with the message "God Bless Our Troops"

## Slide 39: DNS Rebinding Attack
Read permitted: it’s the “same origin”
Firewall
www.evil.com
web server
ns.evil.com
DNS server
171.64.7.115
www.evil.com?
corporate
web server
171.64.7.115 TTL = 0
<iframe src="http://www.evil.com">
192.168.0.100
192.168.0.100
[DWF’96, R’01]
DNS-SEC cannot
stop this attack

## Slide 40: DNS Rebinding Defenses
Browser mitigation: DNS Pinning
  Refuse to switch to a new IP
  Interacts poorly with proxies, VPN, dynamic DNS, …
  Not consistently implemented in any browser
Server-side defenses
  Check Host header for unrecognized domains
  Authenticate users with something other than IP
Firewall defenses
  External names can’t resolve to internal addresses
  Protects browsers inside the organization

## Slide 41: Summary
Core protocols not designed for security
  Eavesdropping, Packet injection, Route stealing, DNS poisoning
  Patched over time to prevent basic attacks
  (e.g. random TCP SN)
More secure variants exist (next lecture) :
IP ⟶ IPsec
DNS ⟶ DNSsec
BGP ⟶ SBGP